## Slide 1: Robot Arm Development
With Moveit motion planner and Galil controller

## Slide 2
Goal

## Slide 3
Overall Framework
Galil Control Card
Action Server
Motor feedback Subscriber
Motor Driver
Motor
Solidworks 3D model
Moveit move group (Core)
Move Group Interface (C++)
GUI
(Rviz Plugin)
Rviz Animation Simulation
(Visualization)
Joint State Publisher
Action Client
Joint State Subscriber
Moveit Function
Galil commander (gclib C++)
URDF
SRDF
Config
Action
Service
Topic
User Interface
Gclib Cmd.
. . .
Application
Moveit & ROS
Based Driver
Pulse
±A ±B
Cmd.
joint_state
Trajectory
Position
Change of joint state
Get IK
Move Group
Action
Plan Path
Exec. Path
Service
Collision Obj.
Attached Obj.
Topic
Simulation
Trajectory

## Slide 4
Install SolidWorks to URDF Exporter from github.
Define Rotation Axes, Coordinates and Limits of each joints.
Follow the sw2urdf GUI, and a ROS package with Rviz demo will be created automatically.
Solidworks Ass. to URDF
Solidworks to URDF tutorials

## Slide 5
Use Moveit setup assistant to create a Moveit package and choose KDL Kinematics Plugin as the kinematics solver.
Drag the end of the arm to the target position and click “Plan & Execute”
Inverse Kinematic Solver
Moveit setup assistant tutorials
Mouse drag
Plan & Execute

## Slide 6
By default, Moveit run on a fake controller to simulate motion on a virtual robot
Substitute the fake controller for our own robot controller to control the real-world robot
Create an action server to process the trajectory message
Moveit
Fake controller
Moveit
Action Client
Joint_State_Subscriber
Moveit Function
Action
Trajectory
Topic
joint_state

## Slide 7
Moveit generate a trajectory with specific positions, velocities and accelerations
Moveit send planned joint trajectory via action
Message type :
trajectory_msgs/JointTrajectoryPoint
  float64[] positions
  float64[] velocities
  float64[] accelerations
  float64[] effort
  duration time_from_start
Joint Trajectory
trajectory_msgs/JointTrajectoryPoint

## Slide 8
Hardware installation
Based Driver
Stepper motor
Ethernet
A+
A-
B+
B-
STEP+
STEP-
DIR+
DIR-
IPC
Step
driver
Galil
control card
Command
Control Current
Pulse
Power supply
24V, GND

## Slide 9
Based Driver
IPC
PSU
Galil control card
Step driver
Step motor

## Slide 10
Position tracking
Galil Controller Solutions
Contour motion
t
x
t
x
Cmd(g, "PT 1");//start pos. tracking mode
Cmd(g, "PT ");//assign an absolute position
//motion start immediately after a PT command
Sleep();//wait motion to complete
Cmd(g, "PT ");//new target position
Sleep();
Cmd(g, "PT ");
Sleep();
Cmd(g, "PT 0");//end of pos. tracking mode
Cmd(g, "CM X");//start contour mode on X-axis
Cmd(g, "CD ");
//write displacement and time step into the buffer
Cmd(g, "CD ");
Cmd(g, "CD ");
Cmd(g, "CD 0=0");//end of contour mode
//motion start after this command
Command Reference

## Slide 11
Position tracking
Error Analysis
Chart: Position-Time graph
asked position | -1598 | -1560 | -1522 | -1484 | -1446 | -1408 | -1370 | -1332 | -1294 | -1256 | -1218 | -1180 | -1142 | -1104 | -1066 | -1027 | -989 | -951 | -913 | -875 | -837 | -799 | -761 | -723 | -685 | -647 | -609 | -571 | -533 | -494 | -456 | -418 | -380 | -342 | -304 | -266 | -228 | -190 | -152 | -114 | -76 | -38 | 0

## Slide 12
Contour motion
Error Analysis
Chart: Position-Time graph
asked position | -1599 | -1560 | -1522 | -1484 | -1446 | -1408 | -1370 | -1332 | -1294 | -1256 | -1218 | -1180 | -1142 | -1104 | -1066 | -1027 | -989 | -951 | -913 | -875 | -837 | -799 | -761 | -723 | -685 | -647 | -609 | -571 | -533 | -494 | -456 | -418 | -380 | -342 | -304 | -266 | -228 | -190 | -152 | -114 | -76 | -38 | 0

## Slide 13
Position tracking
  Pros :
    Control card planning, accurate and stable
    Less error
  Cons :
    Only 32 points can be stored into the buffer
    Time interval need to be a power of 2 (2, 4, 8, …, 256)
Comparation
Contour motion
  Pros :
    Command one point at a time, so there is no limit to the number of planning points
    Can change goals during the motion
  Cons :
    Accumulative error may occur
    The result may be different each time on the same input trajectory

## Slide 14
Obstacle Avoidance

## Slide 15
Move Group C++ Interface allows us to use API to create applications, such as collision detection, obstacle avoidance, and object attachment.
Add a collision object to the world, and then drag the end of the arm to the target position again. Moveit will generate a trajectory bypassing the obstacle.
Rviz visual tool allows us to add and erase collision objects on the GUI panel.
Obstacle Avoidance
Move Group C++ Interface

## Slide 16
Full Demo
demo (streamable.com)

## Slide 17
sw_urdf_exporter/Tutorials - ROS Wiki
【ROS學習】Solidworks模型轉化為URDF檔案格式+三連桿機械臂示例+逆運動學
MoveIt Setup Assistant — moveit_tutorials Noetic documentation (ros-planning.github.io)
ROS中Moveit生成的轨迹如何作用与实际的机械臂(二)
trajectory_msgs/JointTrajectoryPoint
Galil Gclib command reference
References